## Slide 1: EE359 – Lecture 4 Outline
Review of Last Lecture
Model Parameters from Empirical Measurements
Random Multipath Model
Time Varying Channel Impulse Response
Narrowband Fading Model
In-Phase and Quad Signal Components
Auto and Cross Correlation of Received Signal

## Slide 2: Review of Last Lecture
Shadowing
  Log-normal random variable based on CLT applied to many attenuating objects
Combined Path Loss and Shadowing
Cell Coverage Area
  % of locations in a cell meeting a min. SNR criterion
my=0 when average shadowing incorporated into K and g, else my<0
Notes: Lecture notes not consistent with text, should be –psi_dB

## Slide 3: Model Parameters from Empirical Measurements
Fit model to data
Path loss (K,g), d0 known:
  “Best fit” line through dB data
  K obtained from measurements at d0.
  Exponent is MMSE estimate based on data
  Captures mean due to shadowing
Shadowing variance
  Variance of data relative to path loss model (straight line) with MMSE estimate for g
Pr(dB)
log(d)
10g
K (dB)
log(d0)
sy
2

## Slide 4: Statistical Multipath Model
Random # of multipath components, each with
  Random amplitude
  Random phase
  Random Doppler shift
  Random delay
Random components change with time
Leads to time-varying channel impulse response

## Slide 5: Time Varying Impulse Response
Response of channel at t to impulse at t-t:
  t is time when impulse response is observed
  t-t is time when impulse put into the channel
  t is how long ago impulse was put into the channel for the current observation
    path delay for MP component currently observed

## Slide 6: Received Signal Characteristics
Received signal consists of many multipath components
Amplitudes change slowly
Phases change rapidly
  Constructive and destructive addition of signal components
  Amplitude fading of received signal (both wideband and narrowband signals)

## Slide 7: Narrowband Model
Assume delay spread maxm,n|tn(t)-tm(t)|<<1/B
Then u(t)u(t-t).
Received signal given by
No signal distortion (spreading in time)
Multipath affects complex scale factor in brackets.
Characterize scale factor by setting u(t)=ejf0

## Slide 8: In-Phase and Quadrature under CLT Approximation
In phase and quadrature signal components:
For N(t) large, rI(t) and rQ(t) jointly Gaussian by CLT (sum of large # of random vars).
Received signal characterized by its mean, autocorrelation, and cross correlation.
If jn(t) uniform, the in-phase/quad components are mean zero, indep., and stationary.

## Slide 9: Auto and Cross Correlation
Assume fn~U[0,2p]
Recall that qn is the multipath arrival angle
Autocorrelation of inphase/quad signal is
Cross Correlation of inphase/quad signal is
Autocorrelation of received signal is

## Slide 10: Main Points
Path loss and shadowing parameters are obtained from empirical measurements
Statistical multipath model leads to a time-varying channel impulse response
Narrowband model has in-phase and quad. comps that are zero-mean stationary Gaussian processes
  Auto and cross correlation depends on AOAs of multipath