## Slide 1
FIRST AND SECOND-ORDER
TRANSIENT CIRCUITS
IN CIRCUITS WITH INDUCTORS AND CAPACITORS VOLTAGES AND CURRENTS
CANNOT CHANGE INSTANTANEOUSLY.
EVEN THE APPLICATION, OR REMOVAL, OF CONSTANT SOURCES CREATES A
TRANSIENT BEHAVIOR
LEARNING GOALS
FIRST ORDER CIRCUITS
Circuits that contain a single energy storing elements.
Either a capacitor or an inductor
SECOND ORDER CIRCUITS
Circuits with two energy storing elements in any combination

## Slide 2
THE CONVENTIONAL ANALYSIS USING MATHEMATICAL MODELS REQUIRES THE DETERMINATION
OF (A SET OF) EQUATIONS THAT REPRESENT THE CIRCUIT.
ONCE THE MODEL IS OBTAINED ANALYSIS REQUIRES THE SOLUTION OF THE EQUATIONS FOR
THE CASES REQUIRED.
FOR EXAMPLE IN NODE OR LOOP ANALYSIS OF RESISTIVE CIRCUITS ONE REPRESENTS THE
CIRCUIT BY A SET OF ALGEBRAIC EQUATIONS
WHEN THERE ARE INDUCTORS OR CAPACITORS THE MODELS BECOME LINEAR ORDINARY
DIFFERENTIAL EQUATIONS (ODEs). HENCE, IN GENERAL, ONE NEEDS ALL THOSE TOOLS
IN ORDER TO BE ABLE TO ANALYZE CIRCUITS WITH ENERGY STORING ELEMENTS.
ANALYSIS OF LINEAR CIRCUITS WITH INDUCTORS AND/OR CAPACITORS
THE GENERAL APPROACH CAN BE SIMPLIFIED IN SOME SPECIAL CASES WHEN THE FORM
OF THE SOLUTION CAN BE KNOWN BEFOREHAND.
THE ANALYSIS IN THESE CASES BECOMES A SIMPLE MATTER OF DETERMINING SOME
PARAMETERS.
TWO SUCH CASES WILL BE DISCUSSED IN DETAIL FOR THE CASE OF CONSTANT SOURCES.
ONE THAT ASSUMES THE AVAILABILITY OF THE DIFFERENTIAL EQUATION AND A SECOND
THAT IS ENTIRELY BASED ON ELEMENTARY CIRCUIT ANALYSIS… BUT IT IS NORMALLY LONGER
A METHOD BASED ON THEVENIN WILL BE DEVELOPED TO DERIVE MATHEMATICAL MODELS
FOR ANY ARBITRARY LINEAR CIRCUIT WITH ONE ENERGY STORING ELEMENT.
WE WILL ALSO DISCUSS THE PERFORMANCE OF LINEAR CIRCUITS TO OTHER SIMPLE INPUTS
THE MODEL

## Slide 3
AN INTRODUCTION
INDUCTORS AND CAPACITORS CAN STORE ENERGY. UNDER SUITABLE CONDITIONS THIS ENERGY
CAN BE RELEASED. THE RATE AT WHICH IT IS RELEASED WILL DEPEND ON THE PARAMETERS
OF THE CIRCUIT CONNECTED TO THE TERMINALS OF THE ENERGY STORING ELEMENT
With the switch on the left the capacitor receives
charge from the battery.
Switch to the right
and the capacitor
discharges through
the lamp

## Slide 4
GENERAL RESPONSE: FIRST ORDER CIRCUITS
Including the initial conditions
the model for the capacitor
voltage or the inductor current
will be shown to be of the form
Solving the differential equation
using integrating factors, one
tries to convert the LHS into an
exact derivative
THIS EXPRESSION ALLOWS THE COMPUTATION
OF THE RESPONSE FOR ANY FORCING FUNCTION.
WE WILL CONCENTRATE IN THE SPECIAL CASE
WHEN THE RIGHT HAND SIDE IS CONSTANT

## Slide 5
FIRST ORDER CIRCUITS WITH
CONSTANT SOURCES
If the RHS is constant
The form of the solution is
Any variable in the circuit is of
the form
Only the values of the constants
K_1, K_2 will change
TRANSIENT
TIME
CONSTANT

## Slide 6
EVOLUTION OF THE TRANSIENT AND INTERPRETATION OF
THE TIME CONSTANT
A QUALITATIVE VIEW:
THE SMALLER THE THE TIME
CONSTANT THE FASTER THE
TRANSIENT DISAPPEARS
With less than 2% error
transient is zero
beyond this point
Drops 0.632 of initial
value in one time constant
Tangent reaches x-axis in one time constant

## Slide 7
THE TIME CONSTANT
The following example illustrates
the physical meaning of time
constant
Charging a capacitor
The model
The solution can be shown to be
transient
For practical purposes the
capacitor is charged when the
transient is negligible
With less than 1%
error the transient
is negligible after
five time constants

## Slide 8
1. THE CIRCUIT HAS ONLY CONSTANT INDEPENDENT SOURCES
THE DIFFERENTIAL EQUATION APPROACH
CIRCUITS WITH ONE ENERGY STORING ELEMENT
CONDITIONS
2. THE DIFFERENTIAL EQUATION FOR THE VARIABLE OF INTEREST
IS SIMPLE TO OBTAIN. NORMALLY USING BASIC ANALYSIS TOOLS;
e.g., KCL, KVL. . . OR THEVENIN
3. THE INITIAL CONDITION FOR THE DIFFERENTIAL EQUATION
IS KNOWN, OR CAN BE OBTAINED USING STEADY STATE ANALYSIS
SOLUTION STRATEGY: USE THE DIFFERENTIAL EQUATION AND THE
INITIAL CONDITIONS TO FIND THE PARAMETERS

## Slide 9
If the diff eq for y is known
in the form
Use the diff eq to find two
more equations by replacing
the form of solution into the
differential equation
We can use this
info to find
the unknowns
Use the initial condition to get
one more equation
SHORTCUT: WRITE DIFFERENTIAL EQ.
IN NORMALIZED FORM WITH COEFFICIENT
OF VARIABLE = 1.

## Slide 10
(DIFF. EQ. KNOWN,
INITIAL CONDITION KNOWN)
STEP 1 TIME CONSTANT
Get time constant as
coefficient of derivative
STEP 2 STEADY STATE ANALYSIS
IN STEADY STATE THE SOLUTION IS
A CONSTANT. HENCE ITS DERIVATIVE
IS ZERO. FROM DIFF EQ.
Steady state value
from diff. eq.
STEP 3 USE OF INITIAL CONDITION
LEARNING EXAMPLE

## Slide 11
KVL
STEP 1
STEP 2 STEADY STATE
STEP 3 INITIAL CONDITION
LEARNING EXAMPLE

## Slide 12
STEP 1
STEP 2
STEP 3
LEARNING BY DOING

## Slide 13
IT IS SIMPLER TO DETERMINE MODEL
FOR CAPACITOR VOLTAGE
INITIAL CONDITIONS
STEP 1
STEP 2
STEP 3

## Slide 14
KVL(t>0)
STEP 1
LEARNING EXAMPLE
STEP 2: FIND K1 USING STEADY STATE
ANALYSIS
FOR THE INITIAL CONDITION ONE NEEDS
THE INDUCTOR CURRENT FOR t<0 AND
USES THE CONTINUITY OF THE INDUCTOR
CURRENT DURING THE SWITCHING .
THE NEXT STEP REQUIRES THE INITIAL
VALUE OF THE VARIABLE,
THE STEADY STATE ASSUMPTION FOR t<0
SIMPLIFIES THE ANALYSIS

## Slide 15
FOR EXAMPLE USE THEVENIN
ASSUMING INDUCTOR IN STEADY
STATE
KVL
KVL
CIRCUIT IN STEADY STATE (t<0)

## Slide 16
STEP 1
STEP 2
INITIAL CONDITIONS. CIRCUIT IN STEADY STATE t<0
STEP 3
LEARNING EXTENSION

## Slide 17
STEP 1
STEP 2
FOR INITIAL CONDITIONS ONE NEEDS
INDUCTOR CURRENT FOR t<0
CIRCUIT IN STEADY STATE
PRIOR TO SWITCHING
STEP 3
LEARNING EXTENSION

## Slide 18
  USING THEVENIN TO OBTAIN MODELS
Obtain the voltage across the capacitor
or the current through the inductor
Thevenin
KCL@ node a
Use KVL

## Slide 19
EXAMPLE
The variable of interest is the
inductor current. The model is
And the solution is of the form
Next: Initial Condition

## Slide 20
Since K1=0 the solution is
Evaluating at 0+
Loop analysis
Node analysis

## Slide 21
EXAMPLE
Hence, if the capacitor voltage
is known the problem is solved
Model for v_c
Now we need to determine
the initial value v_c(0+)
using continuity and the
steady state assumption

## Slide 22
Continuity of capacitor voltage
Diff Eq
Approach