## Slide 1
LEARNING APPLICATION
HEART PACEMAKER
Simplified SCR model
SCR “fires”
Charging phase
As soon as the SCR switches off the
capacitor starts charging. Hence, assume
Find R so that the SCR is ready to fire
after one second of capacitor charging

## Slide 2
THE DISCHARGE STAGE
With the chosen resistor discharge starts
after one second and the capacitor voltage
is 5V
For SCR turn off
%example6p12
%visualizes one cycle of pacemaker
%charge cycle
tau=0.569;
tc=linspace(0,1,200);
vc=6-5.8*exp(-tc/tau);
%discharge cycle. SCR on
td=linspace(1,1.11,25);
vcd=-22.45+27.45*exp(-(td-1)/tau);
plot(tc,vc,'bd',td,vcd,'ro'),grid,
title('PACEMAKER CYCLE')
xlabel('time(s)'), ylabel('voltage(V)')
legend('SCR off', 'SCR on')

## Slide 3
Inductor current at the beginning of ON period MUST be the same than the current
at the end of OFF period
LEARNING EXAMPLE
BOOSTER CONVERTER
STANDARD DC POWER SUPPLY
BOOSTER “ON” PERIOD
Energy is stored in inductor.
Capacitor discharges
BOOSTER “OFF” PERIOD
Inductor releases energy.
Capacitor charges
e.g. booster

## Slide 4
THE “ON” CYCLE
THE “OFF” CYCLE
SIMPLIFYING ASSUMPTION: THE OUTPUT
VOLTAGE (Vo) IS CONSTANT
By adjusting the duty cycle one can
adjust the output voltage level

## Slide 5
LEARNING BY DESIGN
AFTER SWITCHING WE HAVE RLC SERIES
For the initial conditions analyze circuit
at t=0+. Assume the circuit was in steady
state prior to the switching
Circuit at t=0+

## Slide 6
NOW ONE CAN USE TRIAL AND ERROR
OR CAN ATTEMPT TO ESTIMATE THE
REQUIRED CAPACITANCE
Mesh plot
obtained with
MATLAB
IF FEASIBLE, GET AN IDEA OF THE FAMILY OF SOLUTIONS
» s=[[1:9]';[11:19]'];
» mesh(t,s,ils')
» view([37.5,30])
» xlabel('time(s)'),ylabel('s_1(sec^{-1})')
» title('CURRENT AS FUNCTION OF MODES')
Ils is a matrix that contains all
the computed responses, one
per column

## Slide 7
%example6p14.m
%displays current as function of roots in characteristic equation
% il(t)=(60/(s2-s1))*(exp(-s1*t)-exp(s2*t));
% with restriction s1+s2=20, s1~=s2.
t=linspace(0,5,500)'; %set display interval as a column vector
ils=[]; %reserve space to store curves
for s1=1:19
s2=20-s1;
if s1~=s2
il=(60/(s2-s1))*(exp(-s1*t)-exp(-s2*t));
ils=[ils il]; %save new trace as a column in matrix
end
end
%now with one command we plot all the columns as functions of time
plot(t,ils), grid, xlabel('Time(s)'),ylabel('i(A)')
title('CURRENT AS FUNCTION OF MODES')
Estimate charge by estimating area under the curve
For this curve the area is approx. 12 squares

## Slide 8
%verification
s1=18.944;
s2=20-s1;
il=(60/(s2-s1))*(exp(-s1*t)-exp(-s2*t));
plot(t,il,'rd',t,il,'b'), grid, xlabel('time(s)'), ylabel('i(A)')
title('VERIFICATION OF DESIGN')
Applications