## Slide 1
FOURIER ANALYSIS TECHNIQUES
Fourier series permit the extension of steady state analysis to general periodic
signal.
FOURIER SERIES
LEARNING GOALS
FOURIER TRANSFORM
Fourier transform allows us to extend the concepts of frequency domain to
arbitrary non-periodic inputs

## Slide 2
FOURIER SERIES
The Fourier series permits the representation of an arbitrary periodic signal as
a sum of sinusoids or complex exponentials
Periodic signal
The smallest T that satisfies the previous condition is called the (fundamental)
period of the signal

## Slide 3
FOURIER SERIES RESULTS
Cosine expansion
Complex exponential expansion
Trigonometric series
Phasor for n-th harmonic
Relationship between exponential and trigonometric expansions
GENERAL STRATEGY:
. Approximate a periodic signal using a Fourier series
. Analyze the network for each harmonic using phasors or complex exponentials
. Use the superposition principle to determine the response to the periodic signal

## Slide 4
Original Periodic Signal
Approximation with 2 terms
Approximation with 4 terms
Approximation with 100 terms
EXAMPLE OF
QUALITY OF
APPROXIMATION

## Slide 5
EXPONENTIAL FOURIER SERIES
Any “physically realizable” periodic signal, with period To, can be represented over
the interval by the expression
The sum of exponential functions is always a continuous function. Hence, the right
hand side is a continuous function.
Technically, one requires the signal, f(t), to be at least piecewise continuous. In that
case, the equality does not hold at the points where the signal is discontinuous
Computation of the exponential Fourier series coefficients

## Slide 6
LEARNING EXAMPLE
Determine the exponential Fourier series

## Slide 7
LEARNING EXTENSION
Determine the exponential Fourier series

## Slide 8
LEARNING EXTENSION
Determine the exponential Fourier series

## Slide 9
TRIGONOMETRIC FOURIER SERIES
Relationship between exponential and trigonometric expansions
The trigonometric form permits the
use of symmetry properties of the
function to simplify the computation
of coefficients
Even function symmetry
Odd function symmetry

## Slide 10
TRIGONOMETRIC SERIES FOR FUNCTIONS WITH EVEN SYMMETRY
TRIGONOMETRIC SERIES FOR FUNCTIONS WITH ODD SYMMETRY

## Slide 11
FUNCTIONS WITH HALF-WAVE SYMMETRY
Each half cycle is an inverted copy of the adjacent half cycle
Examples of signals with half-wave symmetry
There is further simplification if the function
is also odd or even symmetric

## Slide 12
LEARNING EXAMPLE
Find the trigonometric Fourier series coefficients
This is an even function with half-wave symmetry

## Slide 13
LEARNING EXAMPLE
Find the trigonometric Fourier series coefficients
This is an odd function with half-wave symmetry
Use change of variable
to show that the two
integrals have the
same value

## Slide 14
LEARNING EXAMPLE
Find the trigonometric Fourier series coefficients

## Slide 15
LEARNING EXTENSION
Determine the type of symmetry of the signals

## Slide 16
LEARNING EXTENSION
Determine the trigonometric Fourier series expansion

## Slide 17
LEARNING EXTENSION
Determine the trigonometric Fourier series expansion
Half-wave symmetry

## Slide 18
Fourier Series Via PSPICE Simulation
1. Create a suitable PSPICE schematic
2. Create the waveform of interest
3. Set up simulation parameters
4. View the results
LEARNING EXAMPLE
Determine the Fourier Series of this
waveform
1. PSPICE schematic
VPWL_FILE in PSPICE library
piecewise linear periodic voltage source
File specifying waveform

## Slide 19
Text file defining corners of piecewise
linear waveform
comments
Use transient analysis
Fundamental
frequency (Hz)

## Slide 20
Schematic used for Fourier series example
To view result:
From PROBE menu
View/Output File
and search until you find the
Fourier analysis data
Accuracy of simulation is affected by
setup parameters.
Decreases with number of cycles
increases with number of points

## Slide 21
FOURIER COMPONENTS OF TRANSIENT RESPONSE V(V_Vs)
DC COMPONENT = -1.353267E-08
HARMONIC FREQUENCY FOURIER NORMALIZED PHASE NORMALIZED
NO (HZ) COMPONENT COMPONENT (DEG) PHASE (DEG)
1 1.000E+00 4.222E+00 1.000E+00 2.969E-07 0.000E+00
2 2.000E+00 1.283E+00 3.039E-01 1.800E+02 1.800E+02
3 3.000E+00 4.378E-01 1.037E-01 -1.800E+02 -1.800E+02
4 4.000E+00 3.838E-01 9.090E-02 4.620E-07 -7.254E-07
5 5.000E+00 1.079E-04 2.556E-05 1.712E-03 1.711E-03
6 6.000E+00 1.703E-01 4.034E-02 1.800E+02 1.800E+02
7 7.000E+00 8.012E-02 1.898E-02 -9.548E-06 -1.163E-05
8 8.000E+00 8.016E-02 1.899E-02 5.191E-06 2.816E-06
9 9.000E+00 5.144E-02 1.218E-02 -1.800E+02 -1.800E+02
10 1.000E+01 1.397E-04 3.310E-05 1.800E+02 1.800E+02
11 1.100E+01 3.440E-02 8.149E-03 -1.112E-04 -1.145E-04
12 1.200E+01 3.531E-02 8.364E-03 1.800E+02 1.800E+02
13 1.300E+01 2.343E-02 5.549E-03 1.800E+02 1.800E+02
14 1.400E+01 3.068E-02 7.267E-03 -3.545E-05 -3.960E-05
15 1.500E+01 3.379E-04 8.003E-05 -3.208E-03 -3.212E-03
16 1.600E+01 2.355E-02 5.579E-03 -1.800E+02 -1.800E+02
17 1.700E+01 1.309E-02 3.101E-03 2.905E-04 2.854E-04
18 1.800E+01 1.596E-02 3.781E-03 -5.322E-05 -5.856E-05
19 1.900E+01 1.085E-02 2.569E-03 -1.800E+02 -1.800E+02
20 2.000E+01 2.994E-04 7.092E-05 1.800E+02 1.800E+02
TOTAL HARMONIC DISTORTION = 3.378352E+01 PERCENT
* file pwl1.txt
* example 14.5
* BECA 7
* ORCAD 9.1
* By J.L. Aravena
0,0
0.1,1
0.2,3
0.3,6
0.4,3
0.5,0
0.6,-3
0.7,-6
0.8,-3
0.9,-1
1.0,0
RELEVANT SEGMENT OF
OUTPUT FILE

## Slide 22
TIME-SHIFTING
It is easier to study the effect of time-shift with the exponential
series expansion
Time shifting the function only changes the phase of the coefficients
LEARNING EXAMPLE

## Slide 23
Time shifting and half-wave periodic signals
Only the odd coefficients of f1 are used

## Slide 24
LEARNING EXTENSION
It was shown before
that for v(t)

## Slide 25
WAVEFORM GENERATION
If the Fourier series for f(t) is known then one can
easily determine the expansion for any time-shifted
and time-scaled version of f(t)
Time scaling does not change the
values of the series expansion
Time-shifting modifies the phase of
the coefficients
The coefficients of a linear combination of signals are the linear combination of
the coefficients
One can tabulate the expansions for some basic waveforms and use them to determine
the expansions or other signals

## Slide 26
Signals with
Fourier series
tabulated in
BECA 8

## Slide 31
LEARNING EXTENSION
From the table of Fourier series
Strictly speaking the value for n=0 must
be computed separately.
Use the table of Fourier series to determine the expansions
of these functions

## Slide 32
FREQUENCY SPECTRUM
The spectrum is a graphical display of the coefficients of the Fourier series.
The one-sided spectrum is based on the representation
The amplitude spectrum displays Dn as the function of the frequency.
The phase spectrum displays the angle as function of the frequency.
The frequency axis is usually drawn in units of fundamental frequency
The two-sided spectrum is based on the exponential representation
In the two-sided case, the amplitude spectrum plots |cn| while the phase spectrum
plots versus frequency (in units of fundamental frequency)
Both spectra display equivalent information

## Slide 33
LEARNING EXAMPLE
The Fourier series expansion, when A=5,
is given by
Determine and plot the first four terms
of the spectrum
Amplitude spectrum
Phase spectrum

## Slide 34
LEARNING EXTENSION
Determine the trigonometric Fourier series and plot the
first four terms of the amplitude and phase spectra
From the table of
series

## Slide 35
STEADY STATE NETWOK RESPONSE TO PERIODIC INPUTS
1. Replace the periodic signal by its Fourier series
2. Determine the steady state response to each harmonic
3. Add the steady state harmonic responses

## Slide 36
LEARNING EXAMPLE

## Slide 37
LEARNING EXTENSION

## Slide 38
AVERAGE POWER
In a network with periodic sources (of the same period) the steady state voltage
across any element and the current through are all of the form
The average power is the
sum of the average powers
for each harmonic

## Slide 39
LEARNING EXTENSION
Determine the average power

## Slide 40
LEARNING EXAMPLE

## Slide 41
FOURIER TRANSFORM
A heuristic view of the Fourier transform
A non-periodic function can be viewed as the limit of a periodic function when the
period approaches infinity

## Slide 42
LEARNING EXAMPLE
Determine the Fourier transform
For comparison we show the spectrum
of a related periodic function

## Slide 43
LEARNING EXAMPLES
Determine the Fourier transform of the
unit impulse function
LEARNING EXTENSION
Determine

## Slide 46
Proof of the convolution property
Exchanging orders of integration
Change integration variable
And limits of integration remain the same

## Slide 47
A Systems application of the convolution property
LEARNING EXTENSION
(And all initial conditions are zero)
From the table of transforms
Use partial fraction
expansion!
The output (response) of a network can
be computed using the Fourier transform

## Slide 48
PARSEVAL’S THEOREM
Think of f(t) as a voltage applied to a one Ohm resistor
By definition, the left hand side is the energy of the signal
Intuitively, if the Fourier transform has a large magnitude over a frequency range
then the signal has significant energy over that range
And if the magnitude of the Fourier transform is zero (or very small) then the
signal has no significant energy in that range
Parseval’s theorem permits the determination of the energy of a signal in a
given frequency range

## Slide 49
LEARNING BY APPLICATION
Examine the effect of this low-pass filter in the
quality of the input signal
One can use Bode plots to visualize
the effect of the filter
High frequencies in the input signal are attenuated
in the output
The effect is clearly visible in the time domain

## Slide 50
The output signal is slower and with less energy than the input signal

## Slide 51
EFFECT OF IDEAL FILTERS
Effect of low-pass filter
Effect of high-pass filter
Effect of band-pass filter
Effect of band-stop filter

## Slide 52
EXAMPLE
AMPLITUDE MODULATED (AM) BROADCASTING
Audio signals do not propagate well in atmosphere – they get attenuated very quickly
Original Solution: Move the audio signals to a different frequency range for broadcasting.
The frequency range 540kHz – 1700kHz is reserved for AM modulated broadcasting
Audio signal
Carrier signals
Broadcasted
signal
AM receivers pick a faint copy of v(t)
Nothing in audio range!

## Slide 53
Audio signal has been AM modulated to the radio frequency range

## Slide 54
EXAMPLE
HARMONICS IN POWER SYSTEMS
Harmonics account for
301.8W or 9.14% of the
total power

## Slide 55
LEARNING BY DESIGN
“Tuning-out” an AM radio station
Fourier transform of signal broadcast
by two AM stations
Fourier transform of received signal
Ideal filter to tune out one AM station
Proposed tuning circuit
Next we show how to design the tuning circuit
by selecting suitable R,L,C

## Slide 56
Designing the tuning circuit
Design equations
Design specifications
Fourier transform of received signal
Ideal filter to tune out one AM station
More unknowns than equations. Make
some choices
Frequency response of circuit
tuned to 960kHz

## Slide 57
LEARNING EXAMPLE
An example of band-pass filter
signal
noise
noise
Proposed
two-stage
band-pass
with two
identical
stages
Design requirement: Make the signal 100 times stronger than the noise

## Slide 58
Equating terms one gets a set of
equations that can be used for design
In a log scale, this filter
is symmetric around
the center frequency.
Hence, focus on 1kHz
1kHz, 100kHz are noise frequencies
10kHz is the signal frequency
Design constraint
After two stages
the noise gain is
1000 times
smaller
Since center frequency is given
this equation constrains the quality factor
We use the requirements to constraint Q

## Slide 59
Resulting Bode plot obtained with PSPICE AC sweep

## Slide 60
Filter output
obtained with
PSPICE
Fourier transform of
output signal obtained
with PSPICE

## Slide 61
EXAMPLE
MULTIPLE FREQUENCY “TRAP” CIRCUIT
BASIC NOTCH FILTER
Multiple frequency trap
Eliminates 10kHz, 20kHz and 30kHz
Tuned for 10kHz
Fourier