## Slide 1: Analog and Digital Filter Design Advanced analog filter design using Matlab
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
Drawback of the classic design
Advanced design paradigm
AFDesign toolbox
AFDSpace toolbox
Example design
MATLAB script Lecture11.m

## Slide 3: Drawback of the classic design
The principal drawback of the classical analog filter design is in returning only one solution
That solution can be unacceptable for many practical implementations
Advanced approach provides
  reduced filter complexity for the desired performance
  better performances for the required complexity

## Slide 4: Advanced design paradigm
Advanced analog filter design introduces straightforward procedures to map the filter specification into a design space, that is, a set of ranges for parameters that we use in the filter design
We search this design space for the optimum solution according to given criteria, such as minimal Q-factor

## Slide 5: Design example
Design a lowpass filter that satisfies the following specification:
Fp = 3000 Hz
Fs = 3225 Hz
Ap = 0.2 dB
As = 40 dB

## Slide 6: Classic design
Fp = 3000;
Fs = 3225;
Ap = 0.2;
As = 40;
Wp = 2*pi*Fp;
Ws = 2*pi*Fs;
[N, Wn] = ellipord(Wp, Ws, Ap, As, 's')
[num,den] = ellip(N, Ap, As, Wn, 's');
f = 1:100:16000;
H = freqs(num, den, 2*pi*f);
plot(f,-20*log10(abs(H)));
[Z,P,K] = ellip(N, Ap, As, Wn, 's');
Qmax = max( -abs(P)./(2*real(P)))
Qmax is unacceptable for implementation

## Slide 7: Advanced design: AFDesign
Qmax is acceptable for implementation

## Slide 8: Design parameters
Design parameters
D = {n, , , fp}
Filter order n
Selectivity factor 
Ripple factor 
Actual passband edge fp

## Slide 9: Design space: AFDSpace

## Slide 10: Design alternative D1
D1 design has higher attenuation in the stopband than is required by the specification. We choose D1 design when we prefer to achieve as large an attenuation as possible in the stopband.

## Slide 11: Design alternative D2
D2 design has lower attenuation in the passband than is required by the specification. We choose this design when we prefer to achieve as low an attenuation as possible in the passband.

## Slide 12: Design alternative D3a
D3a design has the sharpest magnitude response. Disadvantages of D3a can be very high Q-factors and large variation of the group-delay in the passband. This is MATLAB default design.

## Slide 13: Design alternative D3b
D3b design has the sharpest magnitude response. Disadvantages of D3b can be very high Q-factors. The variation of the group delay can be high, but its maximal value can be moved into the transition region, so the group-delay variation can be acceptable in the passband.

## Slide 14: Design alternative D4a
D4a has a smoother magnitude response, and that is the main reason for lower Q-factors and smaller variation of the group delay in the passband.

## Slide 15: Design alternative D4b
D4b has a smoother magnitude response. D4b usually yields very low Q-factors and small variation of the group delay in the passband. D4b has a very low ripple factor.

## Slide 16: Basic alternatives: AFDSpace

## Slide 17: Design subspaces: AFDSpace

## Slide 18: AFDesign

## Slide 19: AFDesign: specification

## Slide 20: AFDesign: D1

## Slide 21: AFDesign: D5 – minimal Q-factor

## Slide 22: AFDesign: Passband, Transition, Stopband

## Slide 23: AFDesign: Summary

## Slide 24: AFDesign: Bandpass

## Slide 25: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/