## Slide 1: Analog and Digital Filter Design Finite precision effects
Miroslav Lutovac and Dejan Tosic

## Slide 2: Overview
Finite wordlength effects
Coefficient quantization
Realizations v. s. quantization
Pole location for quantized coefficients
Overflow arithmetic operations
Limit cycles and overflow oscillations
Dead band effect
Signal quantization error
Roundoff noise
MATLAB examples

## Slide 3: Finite wordlength effects
In custom fixed-point implementations of digital filters, such as VLSI or FPGA implementations, the reduction of accuracy
  saves in chip area and
  increases processing speed
This reduction requires analysis and optimization of the finite wordlength properties:
  coefficient quantization
  rounding or truncation of intermediate results
  arithmetic overflows

## Slide 4: Coefficient quantization
We use coefficient sensitivity to denote the sensitivity of the transfer function (or frequency response, or magnitude response, or phase response) to its coefficients or parameters
Quantized filter coefficients make the transfer function different from the ideal one (with infinite-precision coefficients)
The differences can be predicted by the coefficient sensitivity analysis of a filter

## Slide 5: Realizations v. s. quantization
Many filter realizations can be found for a given transfer function
If we assume that the coefficients are exact, all realizations exhibit the same performances
If coefficients are quantized then performances of the realized filter can differ from the performances of the filter with exact coefficients
Various filter realizations have different amount of degradation after coefficient quantization

## Slide 6: Cascade v. s. allpass IIR
Cascade realization
Allpass realization

## Slide 7: Pole location for quantized coefficients
Direct form realization
Ansari-Liu realization

## Slide 8: Overflow arithmetic operations
In fixed-point arithmetic the result of an arithmetic operation (for example, adding) can exceed the allowed range of numeric values which we call the overflow
Then, a new value from allowed range of numbers must be used for representing the result

## Slide 9: In practice, two rules of replacements are used:
x is the result of an arithmetic operation
y is the number that belongs to the permitted range

## Slide 10: Limit cycles and overflow oscillations
If the input sequence to a digital filter is a constant sequence or if it varies slowly, then the output sequence may oscillate
Those small-amplitude oscillations are caused by rounding errors, or truncating errors, and are called the limit-cycle effects
Overflows generated by additions can result in undesirable large-amplitude oscillations that are called the overflow oscillations
Both limit-cycle oscillations and overflow oscillations settle the filter into the nonlinear mode of operation

## Slide 11: Dead band effect
As a result of roundoff operations, sometimes the output sequence can become constant
If the output sequence does not follow the input sequence the phenomenon is called the dead band effect

## Slide 12: Signal quantization error
In practical digital systems the input sequence can be of higher precision compared to the precision of the DSP system
If the DSP system operates with B bits then we have to quantize the sequence to B bits
The quantization error is the difference between the higher precision sequence value and the value obtained after quantization

## Slide 13: Roundoff noise
When fixed-point arithmetic is used, and quantization to B bits is performed after each multiplication, the variance of output noise is
This type of quantization is called the product quantization

## Slide 14: Finite wordlength effects analysis example
FIR filter

## Slide 15: Specification
N = 22; % Filter order
F = [0 0.4 0.5 1]; % Frequency vector
A = [1 1 0 0]; % Magnitude vector
W = [1 5]; % Weight vector

## Slide 16: Approximation
[b,err,res] = firgr(N,F,A,W);
hfvt = fvtool(b);
firgr computes the filter coefficients b
fvtool is graphical user interface that allows you to analyze digital filters using the handle hfvt

## Slide 17: Realization
H = dfilt.dffir(b);
set(H,'Arithmetic','fixed');
Choose direct-form FIR filter
Specify fixed-point arithmetic
H =
FilterStructure: 'Direct-Form FIR'
Arithmetic: 'fixed'
Numerator: [1x23 double]
PersistentMemory: false
CoeffWordLength: 16
CoeffAutoScale: true
Signed: true
InputWordLength: 16
InputFracLength: 15
OutputWordLength: 16
OutputMode: 'AvoidOverflow'
ProductMode: 'FullPrecision'
AccumMode: 'KeepMSB'
AccumWordLength: 40
CastBeforeSum: true
RoundMode: 'convergent'
OverflowMode: 'wrap';

## Slide 18: Coefficients quantization
H1 = copy(H); % Keep a copy of the original filter
nBits1 = 8; % Use 8 bits for coefficients
set(H1,'CoeffWordLength',nBits1);
H1 =
FilterStructure: 'Direct-Form FIR'
Arithmetic: 'fixed'
Numerator: [1x23 double]
PersistentMemory: false
CoeffWordLength: 8
CoeffAutoScale: true
Signed: true

## Slide 19: Plot response
set(hfvt, 'Filters', [H, H1],'ShowReference','off');
The responses differ

## Slide 20: Generate input sequence
n1 = 1024;
k = 0:n1-1;
f1 = 1/8; f2 = 3/4;
x = sin(2*pi*f1*k) + sin(2*pi*f2*k);
xin = fi(x,true,8,7);
fi returns a fixed-point object with value x, signedness
true, word length 8, and fraction length 7

## Slide 21: Product quantization
H2 = copy(H1);
set(H2,'ProductMode','KeepMSB','ProductWordLength', 8);
H2 = FilterStructure: 'Direct-Form FIR'
Arithmetic: 'fixed'
Numerator: [1x23 double]
PersistentMemory: false
CoeffWordLength: 8
CoeffAutoScale: true
Signed: true
InputWordLength: 16
InputFracLength: 15
OutputWordLength: 16
OutputMode: 'AvoidOverflow'
ProductMode: 'KeepMSB'
ProductWordLength: 8

## Slide 22: Processing
y1 = filter(H1,xin);
y2 = filter(H2,xin);

## Slide 23: Spectrum

## Slide 24: Schematic and response

## Slide 25: Finite wordlength effects analysis example
IIR direct-form I filter

## Slide 26: Specification
N = 9; % Filter order
F = 0.5; % Cutoff frequency
Ap = 0.01; % Maximum passband attenuation
As = 40; % Minimum stopband attenuation

## Slide 27: Approximation
[z,p,k] = ellip(N,Ap,As,F);
[b,a] = ellip(N,Ap,As,F);
H = dfilt.df1(b,a);
hfvt = fvtool(H);
ellip computes the filter
coefficients b and a
fvtool is graphical user interface that allows you to analyze digital filters using the handle hfvt

## Slide 28: Realization
H = dfilt.df1(b,a);
set(H,'Arithmetic','fixed');
Choose direct-form I filter
Specify fixed-point arithmetic
H =
FilterStructure: 'Direct-Form I'
Arithmetic: 'fixed'
Numerator: [1x10 double]
Denominator: [1x10 double]
PersistentMemory: false
CoeffWordLength: 16
CoeffAutoScale: true
Signed: true
InputWordLength: 16
InputFracLength: 15
OutputWordLength: 16
OutputFracLength: 15
ProductMode: 'FullPrecision'
AccumMode: 'KeepMSB'
AccumWordLength: 40
CastBeforeSum: true
RoundMode: 'convergent'
OverflowMode: 'wrap'

## Slide 29: Coefficients quantization
H1 = copy(H); % Keep a copy of the original filter
set(H1,'Arithmetic','fixed','CoeffWordLength',12);
% Use 12 bits for coefficients
H1 =
FilterStructure: 'Direct-Form I'
Arithmetic: 'fixed'
Numerator: [1x10 double]
Denominator: [1x10 double]
PersistentMemory: false
CoeffWordLength: 12

## Slide 30: Plot response
set(hfvt, 'Filters', [H, H1],'ShowReference','off');
The responses differ

## Slide 31: Generate input sequence
n1 = 1024;
k = 0:n1-1;
f1 = 1/8; f2 = 340/1024;
Am = 1/(2^4);
x = Am*sin(2*pi*f1*k) + Am*sin(2*pi*f2*k);
xin = fi(x,true,64,63);
fi returns a fixed-point object with value x, signedness
true, word length 64, and fraction length 63

## Slide 32: Product quantization
H2 = copy(H);
set(H2,'ProductMode','KeepMSB','ProductWordLength', 14);
H2 = FilterStructure: 'Direct-Form I'
Arithmetic: 'fixed'
Numerator: [1x10 double]
Denominator: [1x10 double]
PersistentMemory: false
CoeffWordLength: 32
CoeffAutoScale: true
Signed: true
InputWordLength: 16
InputFracLength: 15
OutputWordLength: 16
OutputFracLength: 15
ProductMode: 'KeepMSB'
ProductWordLength: 14

## Slide 33: Processing
y1 = filter(H,xin);
y2 = filter(H2,xin);

## Slide 34: Spectrum

## Slide 35: Schematic

## Slide 36: Finite wordlength effects analysis example
IIR direct-form II filter

## Slide 37: Realization
H = dfilt.df2(b,a);
set(H,'Arithmetic','fixed');
Choose direct-form II filter
Specify fixed-point arithmetic
H =
FilterStructure: 'Direct-Form II'
Arithmetic: 'fixed'
Numerator: [1x10 double]
Denominator: [1x10 double]
PersistentMemory: false
CoeffWordLength: 16
CoeffAutoScale: true
Signed: true
InputWordLength: 16
InputFracLength: 15
OutputWordLength: 16
OutputFracLength: 15
ProductMode: 'FullPrecision'
AccumMode: 'KeepMSB'
AccumWordLength: 40
CastBeforeSum: true
RoundMode: 'convergent'
OverflowMode: 'wrap'

## Slide 38: Processing
y1 = filter(H,xin);
y2 = filter(H2,xin);

## Slide 39: Spectrum

## Slide 40: Schematic

## Slide 41: Overflow
Overflow occurs when
the input signal has
large values

## Slide 42: Limit cycles
Lecture17IIRdf2limitcycle.m

## Slide 43: Dead band
Lecture17IIRdf2deadband.m

## Slide 44: Further reading
M. D. Lutovac, D. V. Tošić, B. L. Evans
Filter Design for Signal Processing Using MATLAB and Mathematica
Prentice Hall Upper Saddle River, New Jersey ISBN 0-201-36130-2, (c) 2001
http://kondor.etf.bg.ac.yu/~lutovac/